## Slide 1
Los Angeles County
Department of Parks and Recreation
Notes: To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 2: Project Team
California State University Los Angeles
  Students
    Patrick Flinner
    Avik Ghazarian
    Robert Karapetyan
    Aaron Romero
    Ken Shimauchi
    Benjamin Valadez
  Faculty Advisers
    Dr. Russ Abbott
    Dr. Jungsoo Lim
Los Angeles County Department of Parks and Recreation
  Liaison
    Sammy Urbina, Application Developer II

## Slide 3
Oversee over 70,000 acres of parks and open spaces
Manage 182 sites
600 Vehicles
  Difficult to track where vehicles go
  Difficult to control unauthorized vehicle usage
Department of Parks and Recreation

## Slide 5
Bluetooth connection
Internet connection
Future Services
MSSQL Server
Architecture Overview

## Slide 6: Edge Implementation - Components
Raspberry Pi Model 3
  Battery(18650 Li-ion) powered for shutdown purposes
RFID Reader
  HID card Compatibility
  USB Communication
GPS Module
OBD-II connection via Bluetooth
  Python-OBD Library

## Slide 7: Edge Implementation - Raspberry Pi
Raspberry Pi runs 24/7
Determines when a car is moving
  If a car moves, it begin gathering data
  Don’t want to gather data while car is not in use
Raspberry Pi should be able to do everything with limited user interaction

## Slide 8
Edge Implementation - Device
Blender used for Device Case and Power Supply Case 3D model creation
  3D Printed the physical model
Custom Power Supply to run off of 12V car battery
  Step-down Voltage Converter turns 12V to 5V
  2A fuses placed between the Device, PSU, and car battery for circuit protection
16x2 LCD Screen displays Device status to vehicle Driver
  Uses an I2C Backpack module to reduce pinout to just 4 pins

## Slide 9
Uploading Data
Data is on the Raspberry Pi, but how do we send it to the server?

## Slide 10
Apache NiFi to the rescue!
Visual Template Flow
Easy Data Transformation
Easy to get data from Point A to Point B
Notes: Site to Site transmission
Ensures one time delivery: Data is not being reproduced along the way
Data Buffering for IoT devices
Visual Template flow which is uncommon in this space
Easy Transformation from one data format to another
Easy to get data from Point A to Point B

## Slide 11: Network Implementation - Apache NiFi

## Slide 12: Web Application - MSSQL Database

## Slide 13: Web Application - Back End
MSSQL Server
  Transact SQL
  Required admin set ups
.NET Core 2.0
  Service used for the backend
  Platform Independent Web API
Entity Framework Core 2.0
  Translates C# to SQL Queries
  Abstraction through Language Integrated Query
Notes: Problem Statement: A. Persist Data B. Access Data C. Modify Data
Solution: We need a framework that gives us the tools to create a REST API and Persist Data
.NET Core Introduction: Free and Open Source Web Framework (it is modular)
Entity Framework Core Intro: Entity Framework is an object relational mapping module in .NET Core
Linq Intro

## Slide 14: Web Application - Driver

## Slide 15
Web Application - Driver continued…

## Slide 16
This page will show the Driver the trips they selected
Fill out form data for the trips they selected
Web Application - Driver continued…

## Slide 17
Avik Ghazarian

## Slide 18
Avik Ghazarian

## Slide 19
Avik Ghazarian

## Slide 20
Avik Ghazarian

## Slide 21
Avik Ghazarian

## Slide 22: Future Plans
Report generation system for web application
Maximo Integration: Machine Learning to determine when a car will break down
Prevent Vehicle from starting without proper identification
Notes: The Maximo Integration Framework (MIF) is an integral part of the Tivoli Process Automation Engine (TPAE) that allows the synchronization and integration of data and of applications between TPAE and external systems in real time or batch mode by using a variety of communication protocols.

## Slide 23
Questions?
Comments?
Thoughts?