## Slide 1: NASA Robotics competition
CS Members:
  Christian Soltero
  Christopher Portugal
  Jonathan Sahagun
  Jose Ambrosio
  Mikey Thong
ME/EE Members:
  Daniel Solis
  Doroteo Alvarado
  Juan Leguizamon
  Sonia Onofua
Advisors:
  Dr. Jose Macias
  Richard Cross

## Slide 2: Agenda
Introduction and Overview
Rover
ROS
Localization
Mapping
Search
Conclusion

## Slide 3: Swarmathon Background
A robotics competition hosted by University of New Mexico and sponsored by NASA
First held in 2016.
CSULA participated in 2016 and 2017
We will participate in the 2018
Swarmathon is held at Kennedy Space Center
23 Schools across the nation will compete

## Slide 4: Requirements
Requirement | Performance Objective | Source of Requirements | Method of Verification
Operation Time | Prelim – 30 min Semi Final – 30 min Final – 60 mins | Competition | Design
Search Dimensions | Prelim – 15x15 m Semi Final – 22x22 m Final – 22x22 m | Competition | Design
Language | C++ | Customers | Design
Communication | ROS | Competition | Design
Search Objective | Find and as many collect resources in allotted time | Competition | Test
Rover Max Velocity | 1 m/s | Competition | Design

## Slide 5: Swarmathon Goals
Program rovers to:
run autonomously
avoid obstacles
search, collect, and drop-off as many April Cubes into the collection zone

## Slide 6: Competition Rules and Scope
Teams are given 3 Rover
Physical rovers can not be modified
Parts of the given code cannot be modified
Autonomous rovers
Teams have no control over the rover during the competition
The team with the most cubes win
Each round has different amount of rovers, time, and size

## Slide 7: Deliverables and Deadlines
Category | Deliverable Description | Delivery Date
Report | Senior Design Report | 12/06/2017
Technical Check in | GitHub Upload, Form Submission, Video Upload | 12/11/2018
Technical Check in | GitHub Upload, Form Submission, Video Upload | 3/01/2018
Reports Due | Technical And Outreach Reports | 3/15/2018
Activity | Final Code Submission | 3/20/2018
Competition | 2018 Nasa Swarmathon at Kennedy Space Center | 4/17/2018-4/19/2018

## Slide 8: Swarmie (Rovers)
Swarmies are small robotic vehicles
Programmed to communicate and interact as a collective swarm, operate autonomously
Equipped with a computer webcam, ultrasonic sensors, GPS system, motor encoders and servo motors

## Slide 9: Front of the Rover

## Slide 10: Internals of the Chassis

## Slide 11: Rovers connection

## Slide 12: Rover Communication
Communication is done over Wi-Fi using a router.
The rovers connect to a laptop that acts as the master
The software that allows communication is ROS

## Slide 13: ROS (Robot Operating System)
Not an operating system.
It’s a collection of software frameworks for robot software developers.
It is called Robot Operating System because it provides many similar services.
The rovers use roscpp which is a c++ implementation of ROS.

## Slide 14: Benefits of using ROS
Services provided by ROS to diverse computer clusters:
Hardware Abstraction
Low-level device control
Implementation of commonly used functionality
Message passing
Package management

## Slide 15: Message Passing - ROS topics

## Slide 16: Context free diagram

## Slide 17: Context free diagram

## Slide 18: Areas of Focus
Localization
  Most Important
  Without cannot trust rovers to know where they are
Mapping
  Map the area
  Help to avoid obstacle seen by any rover
Search
  Main meat of the project
  Most time will be spent on this part

## Slide 19: Localization
Using an odometer and an IMU
  Calibrating using raw encoder data
  Finding the measurement of error after testing
  How many radians per second in each encoder?
Using GPS and actual data measurement for the location
  Determining where the rover should be in
  Determining if the rover is inside or outside of the GPS area

## Slide 20: Odometer Calibration in 2x2m Square

## Slide 21: Map
Using grid_map ROS package
Take ultrasonic data to make map of what is in front of a rover
Using ROS messages gather all individual data and location data to make a map of the area
This will be used when plotting a path in a known area to take account of obstacle before moving.

## Slide 22: Simultaneous Localization And Mapping
What is SLAM?
  A concept designed to aid autonomous robots become more situated with their surroundings
  Builds a map of an unknown environment while simultaneously navigating through the map
How is it done?
  Through the proper utilization of:
    Localization
    Mapping

## Slide 23: Localization and Mapping
Localization
  An estimated orientation of our robot
    Orientation can include values such as:
      Location on a XY plane
      Angle it is facing
      Landmarks in the immediate vicinity of the robot
Mapping
  Building a model of the environment
  How is mapping done?
    By having input from localization, estimation of the surroundings, keeping tracks of landmarks

## Slide 24: Results of Localization and Mapping
State Estimation
  We are given the robot’s present state and with that information, we can estimate the state of the world
Motion Planning
  In relation to navigation, this is the algorithm the robot refers to when deciding on the most efficient algorithm to get from Point A to Point B
Navigation
  This refers to the robot making its own decisions when a command needs to be fulfilled such as going to a desired location

## Slide 25: The SLAM Problem
Given:
  Robot Controls, Observations
Wanted:
  Map of the Environment, Path of the robot
SLAM is an implementation for autonomous robots, however it has issues
  Implementation
    There is no one formula to implement SLAM. Rather, it must be seen as a concept.
  A map is needed for localization and localization is needed for mapping
    Dynamic algorithm

## Slide 26: Search
Approaches to searching:
  Spiraling
  Lawnmower
  Random
  Divide and Conquer
  Weighted Map Search

## Slide 27: Roomba Search
Roomba
  Efficient cleaning of a room
  Good sensors and movement
Swarmie
  We will only search for a time
  Only front facing sensors and poor ability to fine tune turns
  Current approach is a greedy algorithm. When a cube is found the rover returns it to the collection zone.

## Slide 28: Tools Used

## Slide 29: Conclusion
During winter break:
  We will test more outside
  We will develop most of the algorithm
Next semester:
  We will test and modify the algorithm.

## Slide 30: Thank you