## Slide 1: Sidewalk Slope Monitoring System
Team Members:
Jan Bautista
Hua Chen
Abigail Garcia
Ana Guardado
Cristina Munteanu
Pabasara Navaratne
Alexis Pena
Beatriz Ruiz
Aoqian Wang
Liaisons:
Ted Allen
Alisa Blake
Advisor:
Jungsoo Lim
Russ Abbott
Notes: Good morning everyone! | My name is Alexis pena and I’m the team lead for the Sidewalk Slope Monitoring System Project this year.
Together with my teammates (Name Them) We’ve worked with the city Los Angeles- Bureau of Engineering to pick up where last years team left off.
Our liaisons are Ted Allen and Alisa Blade, however, we’ve had the pleasure of working with many other people on their team
Our Senior Design Advisor is Professor Jungsoo Lim
SO were really excited to tell you more about our accomplishments over the last few months, but first a brief introduction on how the project came to be.

## Slide 2: Introduction
Background
Current Project
Web Application
Image Processing
Rover
Backend Server
Notes: So as previously mentioned, this project first started in 2019 where the Senior Design team then was tasked with creating an affordable, multi tasking rover which can gather and analyze sidewalk data and report its finding back to a an LA city field agent. Removing the manual aspect of having someone go out to the field, measure, and calculate whether a sidewalk has met ADA guidelines, one single stretch of sidewalk at a time
If you take into consideration that sidewalks are prone to break and that Los Angeles has over 11,000 miles of sidewalks-- you can start to visualize why a project like this was considered in the first place. Measuring just one sidewalk is difficult and so keeping 11 thousand miles of sidewalk ADA compliant seems like an impossible task
And so with a working rover prototype provided by the last team, our team was able to pick up right where they left off and we’ve been working on manipulating the rover data and creating the software and infrastructure needed to package everything into a new and improved Rover provided by the Bureau of Engineering.
Our team was assigned 4 important tasks to tackle, the first one being to
Create a web application which would map the data collected by the Rover
Two was to Create a Rover User Interface which would allow a field agent to control said rover
Implement Image processing in order to get an enhanced image and extract useful information
And lastly to, create a backend database to collect, store and manipulating the data I’ll now passing this over to Hua, who will be going over the Web Application side of things.

## Slide 3: Background
BOE maintains approximately 11, 360 miles of sidewalks
Uneven sidewalk – did not settle evenly, tree-root growth, and decay
Pedestrian hazards
Comply with Federal American Disability Act (ADA) standards

## Slide 4: Existing solutions
Digital level
CS8900 Access Profiler
CS8750 Lightweight Survey-Profiler

## Slide 5: Goals for sidewalk slope monitoring System
Crossing slope
Running slope
Vertical Displacement
Horizontal Displacement

## Slide 6
Web Application
Framework
Notes: Therefore we updated the framework to include a navigation bar, additional pages, and a footer to make it look more authentic. As you can see the additional page we have add include a home page, database page, an about page and a page to redirect to a website called navigate LA which displays the layout of LA city. The home and about page gives us additional information of our project, such as why we are doing the project and how it would help the city.
We are currently working on to make django server to host our website. This semester we have finished creating the UI of the website, and next semester we will be implementing the features of the website.
In the next slides, we have another way to display our data, which Ana will introduce.(50 secs)

## Slide 7
Notes: To determine how the sidewalk data should be visualized, we needed to consider the city’s prioritization and scoring system. In their “Sidewalk Repair Program” document, they’ve developed a system that assigns a numerical score to sidewalk segments to determine which sidewalks require immediate attention.
They use a couple of matrices to decide on the numerical score, including the Damage Severity Matrix shown on the top right. For example, the sidewalk segment can receive a severity index score of 5 if the sidewalk slope is higher than 20%, pushing this sidewalk segment higher on the list for repairs.

## Slide 8
Notes: The two criteria we will focus on are cross slope and running slope and their severity indices are identified by their color. In the DWG file on the right, we’ve shown an example of how we can visualize part of the slope-data.
As this task was a new item that had no previous years efforts, the main goal for this semester was to determine how we can visualize the sidewalk data on NavigateLA. This involved finding what application we should, determine how the 3D data like slope can be shown in a 2D manner, and building out sample AutoCAD files.
After completing these items, the next steps involve developing the scripts using AutoCAD’s command language and Python. Considering we do not have sidewalk data currently recorded, we will be collecting sample data and using this to build our scripts. The expectation for the next semester is to develop a few DWG files using our automated scripts.

## Slide 9: Detection of vertical or horizontal displacement
Vertical displacement
Horizontal displacement

## Slide 10: Canny Edge Detection - Image Thresholding

## Slide 11: Image Segmentation - Grabcut Algorithm
Removes noise
Requires user input

## Slide 12: Counting Pixels

## Slide 13: 1. Data collection 2. Data process 3. Data Storage 4. Remote controller
26”
24”
Motor Controller
Raspberry Pi 3
Camera
Digital leveler
Accelerometer
RS232-UART converter
GPS Module
Battery
Screen Cover
Rover
Notes: Data Collection
  Digital level data through RS232-UART interface
  Accelerometer data
  GPS data
Data process
  Read voltage of accelerometer module from register
  Compute vector X, Y respect to Z (gravity)
  Compute X-axis and Y-axis using vector X, Y, Z and trigonometry functions
Data storage
  Stored at onboard flash memory
  Uploaded when the operator returns office
Implemented a remote controller
Accomplished
Completed designing/building chassis
Measure crossing slope and running slope with GPS data
Collect images
Autonomously collect data
Can be controlled remotely

## Slide 14: Rover UI: Data Display & Rover Mode Controls
Latest Rover UI Design 2020
Notes: As previously introduced, we have now integrated two new buttons that have consolidated the rover movement and organized the view for all data that has been collected.
The photo on the left is the rover mode pop up window where we have combined all rover movement functionalities together.Rover Mode has 5 controls that will allow the field workers to move the rover in order to collect data such as to move forward, backward, left, right, stop and control the speed as well.
The photo on the right is the data display which displays all the data that the field workers have collected in one session in a separate window. This table displays the coordinate, time, date, gps location data, orientation, and as well as the pinid, and imageid data.
Now Cristina will go over the previous version of the rover UI and our future plans for the UI during this upcoming winter and spring semester.

## Slide 15: Future Rover and UI
Notes: So in the next slide we are going to talk about future Ui work in Spring
We will be testing the code on the actual LEO ROVER for accuracy once this is assembled
Rover Mode control buttons will be designed for easier recognition ( such as arrows and stop sign)
Data Display mode will have an export mode csv file, so that office users can access it easily.
Data display will be redesigned to save space in displaying the table.
Abigail - Back end Database

## Slide 16: Robecca Leo Rover
Notes: As previously mentioned, the Bureau of Engineering were extremely generous and helped us upgrade our
old rover (Robecca - left) with a much nicer platform, the the Leo (Right) Rover. Were in the process of building the new rover now and the plan would be to implement both the data collection aspect from last year with the newly implemented tasks from this year to have a working Sidewalk monitoring rover for the city of los angeles - bureau of engineering.

## Slide 17: Back-end Database Functionality
Notes: The database is essential as it will be utilized by all aspects of the project .
It links the existing data to new data collected by the rover and field agent .
It provides the storage for the web application to to display the data being used.
It also provides access and stores images from the Gopro and rover to be implemented to the image processing portion.

## Slide 18: Relational Schema
Integrating all sources of data ( GoPro,Rover, NavLA)
Notes: Our relational schema can be visualised by the different sources of data, the leftmost part being the existing data provided by BOE and the Navigate LA website mentioned earlier. This data includes PIN ID’s and asset ID’s which are essential in pinpointing specific properties and sidewalk locations.
Although we have not gotten the rover on the ground for testing, the idea is that Navigate LA data will serve as geographical reference points for the Image data and the rover data listed.
The rightmost data would be extracted from the rover itself such as timestamps and PIN IDs and will be linked to the GoPro Image data.

## Slide 19: Q&A
Thank you
Notes: This concludes the Side Monitoring project Presentation - If you have any question, we’d be happy to answer them now. Thank you