## Slide 1: CSULA - RoboSub
By: Heriberto Gonzalez, Ricardo Medina, Horacio Mondragon, Gabriela Cortes-Mejia, Brandon Pham, Sana Shaikh, Wilson Weng, Kevin Williams, Albert Chew
Ricardo Medina

## Slide 2: What is RoboSub?
Purpose - To foster ties between young engineers and the organizations developing AUV technologies.
Competition Goal - Design an Autonomous Underwater Vehicle (AUV) demonstrate its autonomy by completing a series of tasks.
Competition Sponsors:
Ricardo Medina

## Slide 3: Project Composition
Mechanical/Electrical Engineering Team
Team of 10 Mechanical & Electrical Engineers
Objective:
  Design and construction of the AUV
RoboSub Club Team
Team of undergrads from ME/EE/CS
Objective:
  Build a secondary AUV for the competition
  Learn skills needed for future senior design teams
Computer Science Senior Design Team
Team of 9 Computer Scientists
Objective:
  Design and implementation of AUV Software
Ricardo Medina

## Slide 4: Competition Map
200' by 300' and 38' deep
Ricardo Medina
Ricardo Medina

## Slide 5
Gate Task (Enter the Undead Realm)
Pickups
Paths
Buoy Task (Slay Vampires)
Bins Task (Drop Garlic)
Torpedo Task (Stake through Heart)
Ricardo Medina

## Slide 6
Competition
Requirements
Artificial Intelligence
Object recognition
Autonomous Movement & Navigation
Sensor Data Acquisition
Peripheral controls
Ricardo Medina

## Slide 7: Senior Design Team Breakdown
Mission Planning
Controls
Navigation
Computer Vision
Ricardo Medina

## Slide 8: Mission Planning
Task:
  Communicate with teams to establish what data each subsystems require from others
  Implement the actions required for each task
  Use ROS to interface the subsystems for the AI
Objective:
  Design and implement AI to control the functions of the sub to clear tasks
  To allow the subsystems to interact and transfer requested data so the sub can complete its current objective.
Brandon Pham

## Slide 9: ROS and Smach
Robot Operating System
  Libraries and tools to help with the development of robot applications
  Publishers/Subscribers
    A Publisher continually broadcasts a message
    A Subscriber receives these messages
Smach: A package within ROS
  ROS-independent Python library
  Hierarchical state machines
  Mainly for complex plans
  The state machine on the right is a flow chart that shows different states with given outcomes that determine how the states transition
Brandon Pham

## Slide 10
Wilson Weng

## Slide 11
Wilson Weng

## Slide 12: Controls
The Control Sub-Team's goals are to analyze the Robo-sub control section requirements and to code in Arduino and implement the code.
Hardware Structure and Software:
ROS-Melodic and Arduino IDE
The Robo-sub consists of eight Thrusters.
Four Thrusters purpose are to balance, emerge, and submerge the Robo-sub.
Another four Thrusters purpose make Robo-sub to move forward, backward, left, and right.
Albert Chew

## Slide 13: Software Interfaces
Interface with Navigation System through ROS.
Balance the AUV. Arduino Sketch will subscribe pitch and roll angles from ROS Topic.
Maintain target depth. Arduino Sketch will subscribe depth(distance) from ROS Topic
Move forward or backward. Arduino sketch subscribes distance from ROS Topic.
Change Heading. Arduino sketch subscribes yaw angle from ROS Topic.
Albert Chew

## Slide 14: PID Research
An algorithm that combines proportional, integral and derivative calculation to move a sub from its actual state to its desired state.
Pitch Axis
  The sub tilts forward or backwards
Roll Axis
  The sub moves to the left and right side
YAW
  The sub rotates right and left
Determine proportional, integral, and derivative values
Gaby Cortes

## Slide 15: Controls – Thruster Movement
The red circles represent Roll, while the blue circles represent Pitch. The front and back thrusters are grouped together
The PID controllers will help balance the sub if it tips up or down. The arrows represent the direction the sub will move while balancing
Gaby Cortes

## Slide 16
Gaby Cortes

## Slide 17
Sana Shaikh

## Slide 18: Controls – Angled Thruster Movement
Sana Shaikh

## Slide 19
Controls Code Flowchart
Sana Shaikh

## Slide 20: Navigation
Objective:
  Object Detection
    Output distance from objects
  Object Avoidance
    Provide sensor data to subsystems for decision making
  Pathfinding
    Maneuver AUV to each task
Kevin Williams

## Slide 21
Name: Teledyne Pathfinder DVL
Details:
Tracking Translational Movement
Depth
Python Serial Connection
Name: Bar30 Pressure Sensor
Details:
Pressure reading
Correlates to depth
Used in conjunction with DVL
Arduino Library
I2C connection
Name: AS-1Hydrophones
Details:
Angle to underwater Pinger relative to front of sub
Python Libraries
Reading from Amplifier
Array of Hydrophones connected to amplifier
Name: VectorNav - 100 IMU
Details:
Pitch, Yaw, Roll of sub
C++ library
Serial Connection
Name: Blue Robotics Ping Sonar
Details:
Large object detection
Arduino Library / Python
Navigation: Onboard Sensor
Kevin Williams

## Slide 22
Navigation Overview
Kevin Williams

## Slide 23: Computer Vision
Task:
  Use Convolutional Neural Network to develop a Deep Learning Model to detect and classify objects
  Gather and develop an image dataset of the objects from the competition to be used to train the CNN Model
Objective:
  Object Detection – Be able to detect when an object of interest is present in view of our AUV
  Object Recognition – Classify and Recognize the various objects throughout the course
  Output Objects Estimated Location – Once an object of interest has been Detected and Recognized we should be able to output roughly where in frame our object is at, relative to the angle of the camera
Heriberto Gonzalez

## Slide 24: Deep Learning – Convolutional Neural Networks (CNN)
Convolutional Neural Networks
  Deep Learning algorithm which can take in an input image, assign importance to various aspects/objects in the image and be able to differentiate one from the other
Darknet:
  Darknet is an open-source neural network framework written in C and CUDA
  Allows us to train our CNN using our GPU (Graphics Processing Unit)
YOLOv4:
  Convolutional Neural Network algorithm for real-time object detection
Heriberto Gonzalez

## Slide 25: Computer Vision
The images to help us train the model are thousands of pictures of underwater buoys, bins, and gates.
In the beginning the software mislabeled the buoys. With proper training and modifications to the software we were able have proper classification to have better the accuracy of labeling the buoys.
Horacio Mondragon

## Slide 26
Image Dataset
YOLOv4: 'A' Classifier
Darknet + YOLOv4 Training
OpenLabeling
4 Hours to Train
Heriberto Gonzalez
Avg Fps: 15-20fps

## Slide 27: CSULA - RoboSub
By: Heriberto Gonzalez, Ricardo Medina, Horacio Mondragon, Gabriela Cortes-Mejia, Brandon Pham, Sana Shaikh, Wilson Weng, Kevin Williams, Albert Chew
Ricardo Medina
Thank You!!!